## Slide 1: Noise Analysis: 5-Transistor OTA
Impact of Parasitic Capacitances (C1, C2)
Presented by: Trần Hoàng Minh

## Slide 2: Circuit Model & Assumptions
Circuit Model & Assumptions
  • Circuit: 5-T OTA (PMOS Input M3/M4, NMOS Mirror M1/M2)
  • Key Parasitics:
    - C1 (Mirror Node): Models Cgs + Cdb of M1/M2/M3
    - C2 (Output Node): Load capacitance CL
  • Assumptions:
    - Symmetry: M1=M2, M3=M4
    - Gain: gm·ro >> 1
    - Noise: Channel thermal noise currents only
[Insert your Circuit Diagram Here]

## Slide 3: Key Transfer Functions
Impedance & Transfer Functions
1. Output Impedance (Zout):
  Creates the dominant pole.
  Zout(s) = Rout / (1 + s·Rout·C2)
  where Rout = ro2 || ro4
2. Mirror Transfer Function (Hmir):
  Transfer from M1 (Input) to M2 (Output). Acts as Low-Pass Filter.
  Hmir(s) = i_d2 / i_in1 = 1 / (1 + s·(C1 / gm1))
  Mirror Pole: ω_p1 = gm1 / C1

## Slide 4: Diff Pair & Mirror Noise
Noise Contribution: Pairs M1-M4
• Direct Path (M2, M4):
  - Noise appears directly at output.
  - Transfer Gain = 1
• Mirrored Path (M1, M3):
  - Travels through current mirror (M1 -> M2).
  - Filtered by C1 at high frequencies.
  - Gain = |Hmir(f)|
• PSD Contribution:
  i_out^2 = i_n2^2 + i_n4^2 + (i_n1^2 + i_n3^2) / [1 + (ω·τ1)^2]
  (where τ1 = C1/gm1)

## Slide 5: Tail Current Noise (M0)
Noise Contribution: Tail Source (M0)
• Mechanism:
  - Noise splits equally to differential branches.
  - Path 1 (M4): Direct to output (+).
  - Path 2 (M3): Mirrored and inverted (-).
• Cancellation & Leakage:
  - Low Freq: Perfect cancellation (1 - 1 = 0).
  - High Freq: Phase shift by C1 causes leakage.
• PSD Contribution:
  i_out_tail^2 = (i_n0^2 / 4) * (ω·τ1)^2 / [1 + (ω·τ1)^2]

## Slide 6: Final Result & Conclusion
Total Output Voltage Noise & Conclusion
Total Output Noise PSD (Vo,n^2):
Vo,n^2(f) = |Zout|^2 * ( i_direct^2 + i_mirrored^2 + i_tail^2 )
Key Takeaways:
1. Bandwidth: C2 sets the noise bandwidth.
2. Filtering: C1 reduces noise from M1, M3 at high freq.
3. Tail Noise: M0 noise is zero at DC but increases at high freq due to C1.
Design Note: Minimize C1 to maintain high CMRR at high frequencies.