## Slide 1: Problem 9.20 Solution
Transfer Function and Noise Analysis of First-Order Active Filters

## Slide 2: Part (a): Transfer Function of Circuit I
Circuit I is a standard inverting integrator with a parallel feedback resistor.
  Feedback resistor R_F = 7 kΩ, Input resistor R_in = 7 kΩ
  Feedback capacitor C_F = 80 nF
  The transfer function is given by:
  Vo / Vi = -1 / (1 + jω * R_F * C_F)
  Substituting the values:
  Vo / Vi = -1 / (1 + jω * (7k) * (80n)) --- (1)

## Slide 3: Part (a): Transfer Function of Circuit II
Circuit II is a two-stage circuit. Op-amp 2 is a non-inverting amplifier with a gain of 2.
  Let the output of op-amp 1 be Vx. Then Vo = 2 * Vx, or Vx = Vo / 2.
  Apply KCL at the inverting terminal of op-amp 1 (virtual ground):
  Current through input resistor + Current through feedback resistor + Current through capacitor = 0
  (Vi / 14k) + (Vo / 14k) + (Vx / (1 / (jω * C_F))) = 0
  Substitute Vx = Vo / 2 and C_F = 80nF:
  (Vi / 14k) + (Vo / 14k) + (Vo / 2) * (jω * 80n) = 0

## Slide 4: Part (a): Conclusion
Simplifying the KCL equation for Circuit II.
  Multiply the equation by 14k:
  Vi + Vo + Vo * (jω * 80n * 7k) = 0
  Vi + Vo * (1 + jω * (7k) * (80n)) = 0
  Rearranging for the transfer function:
  Vo / Vi = -1 / (1 + jω * (7k) * (80n)) --- (2)
  Comparing (1) and (2), both circuits have identical transfer functions.

## Slide 5: Part (b): Output Noise for Circuit I
Calculating total output noise using dominant noise sources (resistors).
  Output noise spectral density at DC (from solution):
  V_no^2(0) = [I_n1^2 + I_nF^2] * R_F^2 = (15.2 nV/√Hz)^2
  Total RMS output noise for a single-pole low-pass filter:
  V_no(rms)^2 = V_no^2(0) * [1 / (4 * R_F * C_F)]
  Calculating the RMS value:
  V_no(rms) = V_no(0) / sqrt(4 * R_F * C_F)
  From solution: V_no(rms) = 0.32 μV

## Slide 6: Part (c): Output Noise for Circuit II (Resistors)
Calculating noise from the 14 kΩ resistors (R1 and R2).
  Output noise spectral density at DC is higher due to larger resistors:
  V_no1^2(0) = [I_n1^2 + I_nF^2] * R_F^2 = (21.5 nV/√Hz)^2
  The effective noise bandwidth is determined by R_eff = R_F / 2 = 7k.
  Total RMS output noise:
  V_no1(rms)^2 = V_no1^2(0) * [1 / (4 * (R_F/2) * C_F)]
  From solution: V_no1(rms) = 0.45 μV

## Slide 7: Part (c): Noise Current at Op-amp 2 Input
Analyzing the effect of a noise current source (I_i2) at the negative terminal of op-amp 2.
  The transfer function from I_i2 to Vo is derived as:
  Vo / I_i2 = -R_2 / (1 + 1 / (jω * C_F * R_F / 2))
  Vo / I_i2 = (-jω * R_2 * R_F * C_F / 2) / (1 + jω * C_F * R_F / 2)
  This is a high-pass filter transfer function.
  Conclusion: For ideal white noise, the total output noise due to current noise at this terminal is infinite (∞), as high frequencies are not attenuated.